Achieving Accessible Courthouses

by Dave  Yanchulis

Courthouse Access Advisory Committee.

ourthouses pose unique challenges to accessibility. Most  courtrooms  feature  a  variety  of  elevated spaces  including  witness  stands  and  judges’

benches within areas limited by the well of the court. Even in  new construction, determining the best way to provide access  to these and other spaces can be challenging. Al- though guidelines for courthouses were issued under the Americans with Disabilities Act (ADA) almost a decade

ago and later made part of the International Building Code

(IBC), accessibility has been incremental at best and com- pliance issues remain common.

New guidance developed by an expert panel, the Court- house Access Advisory Committee, is now available and provides effective strategies and solutions for integrating accessibility  into  the  design  of  courthouses.  The  U.S. Access Board, which maintains the ADA Accessibility Guidelines (ADAAG), chartered the committee to promote

greater access to courthouses through the development of

Members of the Courthouse Access

Advisory Committee: 2004–2006

Accessibility Equipment Manufacturers Association Administrative Office of the U.S. Courts American Institute of Architects

American Bar Association

Arizona State Bar Association California Administrative Office of the Courts Conference of State Court Administrators Cook County (IL) Government

David Calvert, P.A. Disability Rights Legal Center District of Columbia Courts Disabilities Law Project

Hearing Loss Association of America

HDR Architecture, Inc. Hellmuth, Obata and Kassabaum, Inc. International Code Council

Lift-U Division, Hogan Manufacturing

Michael Graves & Associates

Michigan Commission for the Blind

Montana Advocacy Program National Association for Court Management National Center for State Courts

National Fire Protection Association

New Hampshire Governor's Commission on Disability

Ninth Circuit for the U.S. Courts Paralyzed Veterans of America PSA-Dewberry, Inc.

Steven Winter Associates, Inc. Superior Court of the District of Columbia T.L. Shield & Associates

Tenth Judicial Circuit Court of Florida

U.S. Department of Justice

U.S. General Services Administration U.S. Judicial Conference, Securities and Facilities Committee

United Spinal Association

32   Building Safety Journal  June 2007

such guidance. The 35-member committee represented an im- pressive cross-section of expertise and experience including courthouse architects, judges, court managers and representatives from ICC and other codes and standards-setting organizations, disability groups and the lift industry, among others.

Over a two-year period, the committee examined design issues, toured  different  types  of  courthouses  across  the  country  and crafted access solutions by consensus. Its recommendations were submitted to the Access Board last November and provide de- tailed guidance on achieving accessible courthouses without compromising traditional design features and requisites. The committee’s report, “Justice for All: Designing Accessible Cour- thouses,” includes best practice recommendations representing the state-of-the-art in accessible courthouse design. Following is a   summary of several of the most widely applicable recommendations. The committee’s full report and related infor- mation are available from the Access Board’s website: www.access-board.gov.

Raised Areas

The leading issue in accessible courthouse design is wheelchair access to raised courtroom areas such as jury boxes, witness stands and judges’ benches. For courts to function properly, these areas must be configured and sufficiently elevated to provide adequate sight lines, decorum and security.

Jury Boxes and Witness Stands

Jury boxes and witness stands are required to be fully accessible in all courtrooms so that people with disabilities can fulfill their responsibilities as jurors and witnesses. Witness stands are typi- cally raised one step and can easily be served by ramps. Depend- ing  upon the configuration and elevations, one ramp can often serve both the witness stand and the jury box. Ramps must be permanent; therefore, portable ramps and flip-down or telescop- ing types are not permitted in new construction.

Wheelchair spaces  are  required  within  the  defined  area  of witness stands and jury boxes (removable seats can also occupy these  spaces).  Sufficient  turning  space  must  be  provided  in witness stands and jury boxes that are accessed by ramps or lifts with entry ramps so that people using wheelchairs can exit in a forward manner. Vertical access to jury boxes can be avoided if front-row seating and the required spaces are provided at floor level, and a side approach is preferable because entrance from the front often requires that a gate in the rail or millwork be operated while maneuvering into and out of the area.

Judges’ Benches and Clerks’ Stations

Access is also required to judges’ benches and stations for clerks and other court personnel. ADAAG permits vertical access to such areas to be provided after construction as needed. Under this “adaptability” option, the requisite space and other features that

Use of Lifts

Both the ADAAG  and the IBC generally limit the use of platform lifts but allow them in courtrooms,  and they have become a common means of providing access to witness stands and judges’ benches. After examining	in-service 	lifts, 	reviewing detailed input from the lift industry and consulting additional  resources  including a government survey of courtroom instal- lations, the Courthouse Access Advisory Committee identified a number of impor- tant considerations.

Common issues affecting lift perform- ance include platform deflection and downward settlement;  interlock  malfunc- tions; and operation requiring assistance such as the removal  of steps, platforms or  millwork.  By  design,  most  courtroom lifts require variances from applicable standards  such  as American  Society  of Mechanical Engineers A18.1, Safety Standard for Platform Lifts and Stairway Chairlifts  (although  it  is  anticipated  that the 2008 edition of the standard will include new specifications  for these and other types of low-rise lifts).

The committee’s report describes avail- able lift technologies and provides recom- mendations  for  improved  performance and compliance. These include proper specification of the interface between lifts and any surrounding millwork, independ- ent operation, the provision of back-up power (required for lifts that are part of an accessible means of egress), and appro- priate maintenance. ◆

June 2007  Building Safety  Journal 33

Achieving Accessible Courthouses (continued)

facilitate later installation of ramps or lifts must be included in courtroom design and construction.

It is important to note that the IBC does not recognize this option and requires full access to these areas, which the Courthouse Access Advisory Committee endorsed as a best practice. A secondary recommendation, intended to reduce the  need for later retrofits, calls for full access to these spaces in at least one courtroom of each type within a court- house and adaptable access in the rest.

For purposes of decorum and security, the committee’s report recommends that vertical access be provided in a manner that allows judges to enter courtrooms at bench level. This can be achieved by locating ramps or lifts in the secured corridor outside the courtroom (which also frees-up space inside the courtroom). If ramps or lifts providing access to the judge’s bench are located in the courtroom, walls or panels should be used to make them less visible.

Spectator Areas

Like other assembly areas, spectator areas in courtrooms must include wheelchair spaces integrated into the seating footprint. In addition, all courtrooms must be equipped with assistive listening systems. The Courthouse Access Advi- sory Committee’s report provides information on available technologies and ways to accommodate spectators with sig- nificant hearing loss as well as those who are deaf. ◆

Dave Yanchulis is Coordinator of Public Affairs for the U.S. Access Board, an independent federal agency that develops and maintains accessibility guidelines and stand- ards for the built environment, transportation vehicles, telecommunications equipment, and electronic and infor- mation technology under the ADA and several other laws, and enforces design standards that cover federally funded facilities.

Update on the New

ADA and ABA Standards

n  the  coming  months,  the  U.S.  Department  of Justice (DOJ) intends to publish a notice to adopt new standards based on updated guidelines issued

by the  U.S. Access  Board  which  will  apply  to  most facilities  covered  by  the Americans  with  Disabilities Act (ADA), including places of public accommodation, commercial facilities, and state and local government facilities. New standards are already in place for trans- portation facilities under the ADA and for most federal facilities, which are covered by an earlier law, the Archi- tectural Barriers Act (ABA).

The Access Board updated the ADA and ABA guide- lines jointly to make them more consistent. In addition, the Access Board harmonized the guidelines with com- panion provisions in the International Building Code (IBC) and applicable referenced standard, ICC/ANSI A117.1, Accessible and Usable Buildings and Facilities, as well as with other model building codes and industry standards (see “2006 IBC ‘Safe Harbor Update’ ” by

Kimberly Paarlberg for more details on IBC and A117.1 harmonization). Once all of the new standards have been adopted, a highly uniform level of accessibility will be specified across the broad spectrum of facilities encom- passed by the ADA and ABA.

The DOJ’s upcoming notice regarding the update of the ADA standards will be available for public comment. In view of the comment period and other regulatory steps that must be completed, final action is likely at least a year  away.  Until  the  new  standards  take  effect,  the

34   Building Safety Journal  June 2007

current standards are to be followed. Under DOJ regu- lations, private sector facilities must meet the original ADA standards, which have changed little since their initial publication in 1991. State and local governments have  the  option  of  following  either  the ADA stan- dards—although certain provisions do not apply—or the Uniform Federal Accessibility Standards (UFAS), which were issued earlier under the ABA.

The Future is Now

It is important to note that transportation facilities and most federally funded facilities are already covered by updated accessibility standards.

The U.S. Department of Transportation (DOT), the other standard-setting agency under the ADA, adopted new standards effective November 2006 which apply to transportation facilities covered by the ADA, including rail stations, bus stops and stations, and airports. These standards are essentially the same as the updated ADA guidelines but include some limited revisions or clarifi- cations concerning provisions for accessible routes, bus

stops, rail station platforms and detectable warnings on curb ramps.

Under  the  ABA,  which  applies  to  facilities  de- signed, built, altered or leased with federal funding, the  General Services Administration (GSA) adopted new standards known as the ABA Accessibility Stand- ards, which generally took effect in May 2006. These standards  apply  to  most  federally  funded  facilities except postal, military and residential facilities. The U.S. Postal Service (USPS) has updated the standards that apply to facilities under its jurisdiction, which be- came effective in October 2005. The Department of Defense  (DOD)  and  Department  of  Housing  and Urban Development (HUD) are still in the process of updating  the  standards  for  military  facilities  and housing. Until then, the UFAS—which all four agen- cies jointly adopted in 1984—governs the design of such facilities.

Copies of the current ADA and ABA guidelines and standards are available on the Access Board’s website at www.access-board.gov. ◆

Current Accessibility Standards

| ADA STANDARDS |
| --- |
| FACILITY TYPE | AGENCY | STANDARDS IN EFFECT |
| places of public accommodation and commercial facilities | DOJ | original ADA standards |
| state and local government | DOJ | original ADA standards or UFAS* |
| transportation | DOT | new standards took effect November 29, 2006 |
| * Current DOJ regulations permit use of the ADA standards (although some provisions, such as the elevator exception, do not apply) or UFAS. |
| ABA STANDARDS |
| FACILITY TYPE | AGENCY | STANDARDS IN EFFECT |
| federally funded (except postal, military, and residential) | GSA | new standards took effect May 8, 2006 (February 6, 2007 for leased facilities) |
| postal | USPS | new standards took effect October 1, 2005 |
| military | DOD | UFAS |
| residential | HUD | UFAS |

June 2007  Building Safety  Journal 35

# Text boxes

C

I